## Slide 1
Introduction
Arduino is an open-source electronic prototyping platform based on a simple i/o board and a development environment for writing software for the board.

## Slide 2: Arduino Board
“Strong Friend” Created in Ivrea, Italy
in 2005 by Massimo Banzi & David Cuartielles
Open Source Hardware
Processor
Coding is accessible & transferrable  (C++, Processing, java)

## Slide 3: What is a Microcontroller
A small computer on a single chip
  containing a processor, memory, and input/output
Typically "embedded" inside some device that they control
A microcontroller is often small and low cost
www.mikroe.com/chapters/view/1

## Slide 4: Getting Started
SW Installation: Arduino (v.1.0+)
Drivers (FTDI)
Guide
Materials: Guide
        Analog I/O, Digital I/O, Serial, & Fritzing handouts
        Arduino CheatSheet

## Slide 5
Analog INPUTS
Digital I\O
PWM(3, 5, 6, 9, 10, 11)
PWR IN
USB
(to Computer)
SCL\SDA
(I2C Bus)
POWER
5V / 3.3V / GND
RESET
Notes: Look up analog ref

## Slide 6: Pin Description

## Slide 7: Pin Description

## Slide 8: Technical Specs

## Slide 9: Arduino Shields
PCB
Built Shield
Inserted Shield

## Slide 10: Arduino Shields
Micro SD
MP3 Trigger
LCD

## Slide 11: SIK Components (SparkFun Inventor Kit)
Push Button |  | Digital Input | Switch - Closes or opens circuit | Polarized, needs resistor
Trim potentiometer |  | Analog Input | Variable resistor | Also called a Trimpot.
Photoresistor |  | Analog Input | Light Dependent Resistor (LDR) | Resistance varies with light.
Relay |  | Digital Output | Switch driven by a small signal | Used to control larger voltages
Temp Sensor |  | Analog Input | Temp Dependent Resistor | 
Flex Sensor |  | Analog Input | Variable resistor | 
Soft Trimpot |  | Analog Input | Variable resistor | Careful of shorts
RGB LED |  | Dig & Analog Output | 16,777,216 different colors | Ooh... So pretty.
Name | Image | Type | Function | Notes

## Slide 12: SIK Components

## Slide 13: SIK Components

## Slide 14: SIK Components

## Slide 16: Using the Breadboard to built a simple circuit
Use the breadboard to wire up a single LED with a 330 Ohm Resistor (Orange-Orange-Brown).
Note: the longer leg on the LED is the positive leg and the shorter leg is the negative

## Slide 17: Fritzing View of Breadboard Circuit
What happens when you break the circuit?
What if you wanted to add more than one LED?

## Slide 18: Concepts: INPUT vs. OUTPUT
Referenced from the perspective of the microcontroller (electrical board).
Inputs is a signal / information going into the board.
Output is any signal exiting the board.
Almost all systems that use physical computing will have some form of output
What are some examples of Outputs?

## Slide 19: Concepts: INPUT vs. OUTPUT
Referenced from the perspective of the microcontroller (electrical board).
Inputs is a signal / information going into the board.
Output is any signal exiting the board.
Examples: Buttons Switches, Light Sensors, Flex Sensors, Humidity Sensors, Temperature Sensors…
Examples: LEDs, DC motor, servo motor, a piezo buzzer, relay, an RGB LED

## Slide 20: Concepts: Analog vs. Digital
Microcontrollers are digital devices – ON or OFF. Also called – discrete.
analog signals are anything that can be a full range of values. What are some examples? More on this later…
5 V
0 V
5 V
0 V

## Slide 21: Open up Arduino
Hints:
For PC Users 
Let the installer copy and move the files to the appropriate locations, or
Create a folder under C:\Program Files (x86) called Arduino. Move the entire Arduino program folder here.
For Mac Users 
Move the Arduino executable to the dock for ease of access.
Resist the temptation to run these from your desktop.

## Slide 22: Arduino Integrated Development Environment (IDE)
Two required functions / methods / routines:
void setup()
{
// runs once
}
void loop()
{
// repeats
}
error & status messages
Notes: Be sure to point out the what all of the buttons do.

## Slide 23: Arduino programming structure

## Slide 24: Settings: Tools  Serial Port
Your computer communicates to the Arduino microcontroller via a serial port  through a USB-Serial adapter.
Check to make sure that the drivers are properly installed.
Notes: All connections to computers- mice, printers etc use a serial port. Gotta pick the right one.

## Slide 25: Settings: Tools  Board
Next, double-check that the proper board is selected under the ToolsBoard menu.
Notes: All connections to computers- mice, printers etc use a serial port. Gotta pick the right one.

## Slide 26
digitalWrite()
analogWrite()
digitalRead()
if() statements / Boolean
analogRead()
Serial communication
This work is licensed under a Creative Commons Attribution-ShareAlike 3.0 United States License.
BIG 6 CONCEPTS

## Slide 27: Let’s get to coding…
Project #1 – Blink
  “Hello World” of Physical Computing
Psuedo-code – how should this work?
Turn LED ON
Wait
Turn LED OFF
Wait
Rinse & Repeat

## Slide 28: Comments, Comments, Comments
Comments are for you – the programmer and your friends…or anyone else human that might read your code.
// this is for single line comments
// it’s good to put a description at the top and before anything ‘tricky’
/* this is for multi-line comments
Like this…
And this….
*/

## Slide 29
comments
Notes: Review the two main parts of the sketch – void setup() and void loop()
Provide rationale for good commenting.
Emphasize the need for good / clean coding practices like indenting.

## Slide 30: Three commands to know…
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(13, OUTPUT);
digitalWrite(pin, HIGH/LOW);
ex: digitalWrite(13, HIGH);
delay(time_ms);
ex: delay(2500); // delay of 2.5 sec.
// NOTE: -> commands are CASE-sensitive
Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.

## Slide 31: Load the program to the Arduino board

## Slide 32: Project #1: Wiring Diagram
Move the green wire from the power bus to pin 13 (or any other Digital I/O pin on the Arduino board.
Image created in Fritzing

## Slide 33: A few simple challenges Let’s make LED#13 blink!
Challenge 1a – blink with a 200 ms second interval.
Challenge 1b – blink to mimic a heartbeat
Challenge 1c – find the fastest blink that the human eye can still detect…
1 ms delay? 2 ms delay? 3 ms delay???

## Slide 34: Try adding other LEDs

## Slide 35: Programming Concepts: Variables
Variable Scope
Global
---
Function-level

## Slide 36: Programming Concepts: Variable Types
Variable Types:
8 bits
16 bits
32 bits
byte
char
int
unsigned int
long
unsigned long
float

## Slide 37: Fading in and Fading Out (Analog or Digital?)
A few pins on the Arduino allow for us to modify the output to mimic an analog signal.
This is done by a technique called:
Pulse Width Modulation (PWM)

## Slide 38: Concepts: Analog vs. Digital
To create an analog signal, the microcontroller uses a technique called PWM. By varying the duty cycle, we can mimic an “average” analog voltage.
Pulse Width Modulation (PWM)

## Slide 39: Project #2 – Fading Introducing a new command…
analogWrite(pin, val);
pin – refers to the OUTPUT pin (limited to pins 3, 5, 6, 9, 10, 11.) – denoted by a ~ symbol
val – 8 bit value (0 – 255).
0 => 0V | 255 => 5V

## Slide 40: Move one of your LED pins over to Pin 9
In Arduino, open up:
File  Examples  01.Basics  Fade

## Slide 41: Fade - Code Review

## Slide 42: Fade - Code Review

## Slide 43: Project# 2 -- Fading
Challenge 2a – Change the rate of the fading in and out. There are at least two different ways to do this – can you figure them out?
Challenge 2b – Use 2 (or more) LEDs – so that one fades in as the other one fades out.

## Slide 44: Color Mixing Tri-color LED
In the SIK, this is a standard – Common Cathode LED
This means the negative side of the LED is all tied to Ground.
R
G
B

## Slide 45: Project 3 – RGB LED
Note: The longest leg of the RGB LED is the Common Cathode. This goes to GND.
Use pins 5, 6, & 9

## Slide 46: How many unique colors can you create?
Use Colorpicker.com or experiment on your own.
Pick out a few colors that you want to try re-creating for a lamp or lighting display...
Play around with this with the analogWrite() command.

## Slide 47: RGB LED Color Mixing
int redPin = 5;
int greenPin = 6;
int bluePin = 9;
void setup()
{
pinMode(redPin, OUTPUT);
pinMode(greenPin, OUTPUT);
pinMode(bluePin, OUTPUT);
}

## Slide 48: RGB LED Color Mixing
void loop()
{
analogWrite(redPin, 255);
analogWrite (greenPin, 255);
analogWrite (bluePin, 255);
}

## Slide 49: Driving Motors or other High Current Loads
NPN Transistor (Common Emitter “Amplifier” Circuit)
to Digital
Pin 9

## Slide 50: Input
Input is any signal entering an electrical system .
Both digital and analog sensors are forms of input
Input can also take many other forms: Keyboards, a mouse, infrared sensors, biometric sensors, or just plain voltage from a circuit

## Slide 51: Project #4 – Digital Input
In Arduino, open up:
File  Examples  02.Digital  Button

## Slide 52: Digital Sensors (a.k.a. Switches) Pull-up Resistor (circuit)
to Digital Pin 2

## Slide 53: Digital Sensors (a.k.a. Switches) Add an indicator LED to Pin 13
This is just like our 1st circuit!

## Slide 54: Digital Input
Connect digital input to your Arduino using Pins # 0 – 13 (Although pins # 0 & 1 are also used for programming)
Digital Input needs a pinMode command:
pinMode (pinNumber, INPUT);
Make sure to use ALL CAPS for INPUT
To get a digital reading:
int buttonState = digitalRead (pinNumber);
Digital Input values are only HIGH (On) or LOW (Off)
Notes: Put together circuit # 7 and leave in

## Slide 55: Digital Sensors
Digital sensors are more straight forward than Analog
No matter what the sensor there are only two settings: On and Off
Signal is always either HIGH (On) or LOW (Off)
Voltage signal for HIGH will be a little less than 5V on your Uno
Voltage signal for LOW will be 0V on most systems

## Slide 56
http://opensourcehardwarejunkies.com/tutorial-03-digitalread-and-serial-port-communication/

## Slide 57: Programming: Conditional Statements if()

## Slide 58: Programming: Conditional Statements if()
void loop()
{
int buttonState = digitalRead(5);
if(buttonState == LOW)
{ // do something
}
else
{ // do something else
}
}
DIG INPUT

## Slide 59: Boolean Operators
<Boolean> | Description
( ) == ( ) | is equal?
( ) != ( ) | is not equal?
( ) > ( ) | greater than
( ) >= ( ) | greater than or equal
( ) < ( ) | less than
( ) <= ( ) | less than or equal

## Slide 60: Trimpot (Potentiometer) Variable Resistor
wiper
fixed
end
fixed
end

## Slide 61: Analog Sensors 3 Pin Potentiometer = var. resistor (circuit) a.k.a. Voltage Divider Circuit
1.0 V
1.0 V
wiper
fixed
ends

## Slide 62: analogRead()
Arduino uses a 10-bit A/D Converter:
this means that you get input values from 0 to 1023
  0 V  0
  5 V  1023
Ex:
int sensorValue = analogRead(A0);

## Slide 63: analogRead()

## Slide 64: Using Serial Communication
Method used to transfer data between two devices.
Arduino dedicates Digital I/O pin # 0 to receiving and Digital I/O pin #1 to transmit.
Data passes between the computer and Arduino through the USB cable. Data is transmitted as zeros (‘0’) and ones (‘1’) sequentially.
Notes: For this reason, we typically do not use Digital I/O 0 or 1 for anything in our designs.

## Slide 65: Serial Monitor & analogRead()
Initializes the Serial Communication
9600 baud data rate
prints data to serial bus

## Slide 66: Serial Monitor & analogRead()
Opens up a Serial Terminal Window

## Slide 67: Analog Sensors 2 Pin Analog Sensors = var. resistor
Take two sensors -- Use the Serial Monitor and find the range of input values you get for each sensor.
MaxAnalogRead = _________
MinAnalogRead = _________

## Slide 68: Analog Sensors
Examples:
Sensors | Variables
Mic | soundVolume
Photoresistor | lightLevel
Potentiometer | dialPosition
Temp Sensor | temperature
Flex Sensor | bend
Accelerometer | tilt/acceleration

## Slide 69: Additional Serial Communication Sending a Message
void loop ( )
{
Serial.print(“Hands on “) ;
Serial.print(“Learning ”) ;
Serial.println(“is Fun!!!”) ;
}

## Slide 71: Serial Communication: Serial Debugging
void loop()
{
int xVar = 10;
Serial.print ( “Variable xVar is “ ) ;
Serial.println ( xVar ) ;
}

## Slide 72: Serial Communication: Serial Troubleshooting
void loop ( )
{
Serial.print (“Digital pin 9: “);
Serial.println (digitalRead(9));
}

## Slide 73
Questions?